## Slide 1
TELIPORT SEASON 4 · TATA ELXSI · CASE STUDY 2
PackForge
A design workbench for battery packs that finds the hot-charge problem before the hardware does.
Falak Anwar · Zaid Alam
Reusable Digital Platform for Designing Battery Energy Systems
Notes: Open with the question every e-scooter owner in an Indian summer faces: can I charge right after the ride? PackForge is a small, working, validated workbench that answers that for any pack design, before hardware is built. The picture is illustrative: a 13S10P pack, hot in the middle, with the two sensors the baseline BMS relies on sitting on cooler corner cells.

## Slide 2
PROBLEM UNDERSTANDING
One pack, one hard day
Application
48 V pack for an urban e-scooter. Baseline: 13S10P NMC 21700, 2,263 Wh usable.
Operating case
40 °C ambient. Plugged in straight after the ride, so the charge starts from the pack’s end-of-ride state.
Scope boundary
One low-voltage pack: cells, cooling, sensing, protection and BMS control. No high-voltage system.
ID | Requirement | Limit | Type
REQ-01 | Nominal voltage fits 48 V controller | 44–56 V | must
REQ-02 | Usable energy, urban cycle at 40 °C | ≥ 2,000 Wh | must
REQ-03 | Cell temperature while charging | ≤ 45 °C | must
REQ-04 | Cell temperature while riding | ≤ 55 °C | must
REQ-05 | Charge time, plug-in → 80 % | ≤ 120 min | should
REQ-06 | Cell-to-cell temperature spread | ≤ 5 K | should
REQ-07 | Blind spot: hottest cell − BMS view | ≤ 3 K | should
REQ-08 | Pack mass | ≤ 16 kg | should
REQ-09 | Pack volume | ≤ 12 L | should
REQ-10 | Pack cost | ≤ ₹60,000 | should
REQ-11 | Cycle life in hot climate | ≥ 1,000 cycles | should
Shaded rows: where the baseline gets into trouble.
PackForge · requirements from studies/escooter_48v/study.json
2
Notes: Problem understanding. The study is one 48 V e-scooter pack on the hardest realistic day: 40 °C ambient and plugged in straight after the ride. Must-requirements disqualify a design; should-requirements become stated risks. The shaded rows — charge temperature, charge time, blind spot — are where the baseline gets into trouble. Charge time is plug-in to 80 % including any thermal hold, because that is what the rider waits for.

## Slide 3
THE PROBLEM · BASELINE AFTER A RIDE
The BMS can’t see the hottest cell
3.2 K
The hottest cell runs this far above what the two NTCs read. REQ-07 allows 3 K.
48 min
Thermal hold after plug-in: no current until the sensors cool into the derate window.
47.6 °C
Then interior cells charge above their 45 °C limit. REQ-03 fails, and nothing on the BMS shows it.
The brief’s “propagates unpredictably from cell to system” — visible only with cell-level modelling.
Illustrative 13S10P pack. Rings: the two BMS sensors, on cooler corner cells. The simulated field is in the app’s Heat map tab.
Source: PackForge CLI run, baseline, charge after drive at 40 °C ambient
3
Notes: After the ride the cells next to the sensors cool first, so the two NTCs under-read the hottest cell by 3.2 K. The BMS waits 48 minutes in a thermal hold — no current — then starts charging and derates on the NTCs, while interior cells reach 47.6 °C, above the 45 °C charge limit. No alarm, no trip: the BMS simply cannot see it. All three numbers come from the CLI run of the baseline. The drawing is illustrative; the simulated heat map is in the app.

## Slide 4
THE PHYSICS LIMIT
No firmware beats the passive floor
40 °C
ambient
5 K
headroom for all the charge heat
45 °C
cell charge limit (REQ-03)
+
=
≥ 139 min
Hand calc, 10 → 80 %, passive NMC pack, even from a cold start: full current to the limit, then the current that holds it there.
161 min
Simulated 10 → 80 % after a ride. The sim and the independent bound agree; a test enforces it.
So the fix is hardware — better cooling (A) or a cooler-running cell (B). Firmware (C) can make charging safe, not faster.
Source: PackForge CLI — thermal-limit charge bound (hand calc) vs simulated 10–80 % charge, baseline
4
Notes: At 40 °C ambient the 45 °C limit leaves only 5 K for every joule of charge heat. An independent hand calculation — the ideal profile for an interior cell: full current until it reaches the limit, then exactly the current that holds it there — says a passive NMC pack needs at least 139 minutes for 10 to 80 %, even from a cold start. The simulation gives 161 minutes after a ride. A test keeps the simulation within 0.95 to 1.3 times the bound on a cold start. No firmware can beat this floor; only moving heat out or making less of it can.

## Slide 5
DESIRABILITY
Built for people who design packs
Students and new engineers
See why a design fails: every conflict comes with its cause chain across cell, thermal and BMS, plus candidate fixes.
Pack engineers
Screen design options before hardware: same requirements, same scenarios, ranked with evidence levels and risks stated.
PAIN POINTS WE REMOVE
Siloed data
Electrical, thermal and BMS models with copied parameters. Here they share one design file.
Late conflicts
A blind spot like the baseline’s shows up on the first hot prototype. Here it shows up on paper.
Hot-climate safety
E-2W packs in India charge in 40 °C heat, often right after a ride — the case we design for.
PackForge · users and pain points
5
Notes: Desirability. Two users: students and new engineers learning trade-offs, and pack engineers screening options early. The pains: data split across tools, conflicts found late on hardware, and the hot-climate charging case that matters for Indian two-wheelers.

## Slide 6
THE PLATFORM · REUSABLE FOR ANY CELL AND LAYOUT
One design file feeds every model
1
Design (JSON)
Cell, S×P layout, cooling, sensing, protection, control. Options hold only their diffs.
2
Electro-thermal sim + BMS
1-RC model and one thermal node per cell; CC-CV, derating, OV/UV/OT protection.
3
KPIs with evidence
Every number tagged from datasheet up to measured.
4
Conflict checker
11 requirements and 14 interface rules, each failure with a cause chain and fixes.
5
Rank and report
Three answers, 2× heat re-run, traceability, offline HTML report.
Any cell chemistry, any S×P layout, any cooling and sensor layout.
A new option is a JSON file with only its differences from the baseline.
Subsystems exchange values only through the design and the metrics — the brief’s “consistent parameter exchange”.
PackForge · Python package packforge/ · Streamlit UI · CLI
6
Notes: How it works. One design file is the single source of truth. Every design option is a small JSON file that extends the baseline with only its differences. The simulator runs the drive, then the charge from the drive’s end state, with a BMS that only knows what its sensors tell it. Every KPI carries an evidence level. The conflict checker turns failures into cause chains and fixes. Nothing here is specific to scooters: a new cell, study or rule is a data file, not code.

## Slide 7
EVIDENCE · MEASURED (PROXY)
Checked on 60 logs it never saw
NMC cell fitted on public data for a proxy cell (LG M50LT, drilled for an internal thermocouple) at 25 and 35 °C. Hold-out at 45 °C: 3 cells × (10 drives + 10 charges), never used in the fit.
Hold-out set | Logs | V RMSE, SOC ≥ 10 % (median / max) | V RMSE, full range | T RMSE (median) | T rise meas / model
Drive cycles | 30 | 18 / 43 mV | 38 / 122 mV | 0.23 K | 2.0 / 1.0 K
1C charges | 30 | 17 / 22 mV | 22 / 25 mV | 0.55 K | 3.4 / 1.6 K
Voltage holds at a temperature the fit never saw — so the heat the model generates is credible.
Temperature rise is under-predicted ~2× (no SOC-dependent resistance or entropic heat). So every design is re-run at 2× heat.
Calibrated vs generic: R0 0.0267 vs 0.020 Ω · R1 0.0230 vs 0.012 Ω · τ 46 vs 30 s · capacity 4.874 vs 5.0 Ah. Test-rig cooling is fitted but never carried over to a pack.
Data: Yao, Droese, Kowal — TU Berlin, DOI 10.14279/depositonce-25110, CC BY 4.0
7
Notes: Evidence. The NMC cell is calibrated on a proxy cell — the LG M50LT from the public TU Berlin internal-temperature dataset — not the cell we would buy. Fit at 25 and 35 °C, hold-out at 45 °C: 60 logs never used in the fit. Voltage error is 17–18 mV median in the operating window, so heat generation holds at an unseen temperature. Be upfront: the temperature rise is under-predicted about 2×, which is why the robustness run uses 2× heat. The chamber’s cooling is a test-rig parameter and is never transferred to a pack. The LFP cell used in Option B is not validated.

## Slide 8
ENGINEERING QUALITY
Every result is cross-checked
Cell: OCV(SOC) + R0 + one RC branch, Arrhenius temperature scaling. Thermal: one node per cell, I²R heat, loss to the sink via h × surface, 4-neighbour conduction. Every assumption has an ID, a source and the results it affects.
± 2 %
Adiabatic heat balance: heat generated matches the cells’ temperature rise.
0.9–1.06×
Delivered energy vs nominal, ending on the undervoltage cut-off.
≤ 0.4 %
KPI change from a 2 s to a 1 s time step (ΔT within 0.05 K).
0.95–1.3×
Simulated charge time vs the independent hand-calc bound, cold start.
≤ 45 °C
Observer-controlled charge peak with ±30 % error in its cooling model.
23 tests
Physics, conflicts, calibration, ranking and report, run in ~90 s.
Source: tests/test_packforge.py · model conventions in CLAUDE.md
8
Notes: Engineering quality. The model is deliberately simple and stated: an equivalent-circuit cell with one RC branch and Arrhenius scaling, and one thermal node per cell. What makes it trustworthy is the checks: heat balance within 2 %, energy within 0.9–1.06× of nominal, time-step convergence, an independent hand calculation, an observer robustness check, and 23 automated tests that guard all of it. Every placeholder value is an assumption with an ID that the traceability tab links to the results it affects.

## Slide 9
RESULTS · 40 °C, PLUGGED IN RIGHT AFTER THE RIDE
Four designs, one study, same scenarios
Chart: Charge time, plug-in → 80 % (min)
| Baseline · 244 min | A: NMC + Al plate · 92 min | B: LFP 16S8P · 97 min | C: + observer · 277 min
Thermal hold | 48.2 | 0 | 0 | 89.5
Charging | 195.5 | 92.1 | 97.4 | 187.1
Metric | Base | A | B | C
Peak T, charging | 47.6 °C fail | 44.0 °C | 43.7 °C | 44.5 °C
Peak T, riding | 53.4 °C | 44.1 °C | 43.1 °C | 53.4 °C
Blind spot | 3.2 K warn | 0.0 K | 0.1 K | 0.2 K
Pack mass | 12.3 kg | 13.5 kg | 22.7 kg warn | 12.3 kg
₹ / usable kWh | 23.1 k | 24.8 k | 18.2 k | 23.1 k
Cycle life (est.) | ~370 | ~405 | ~1,290 | ~370
Ranking | disqualified | 2nd | 1st | 3rd
Cycle life is a rule of thumb (not validated); costs and masses are generic class values. B’s LFP cell is not validated.
Source: python -m packforge (studies/escooter_48v), calibrated NMC cell
9
Notes: Same study, same scenarios, four designs. The orange part of each bar is the thermal hold — time plugged in with no current. The baseline is disqualified: it charges at 47.6 °C. A adds an aluminium conduction plate and six centre NTCs; B switches to LFP; C keeps the baseline hardware and only changes the BMS to derate on a thermal observer — a virtual hotspot sensor. C is safe but slowest, because it honestly waits for the hotspot to cool. Calibrating the NMC cell changed the numbers (the hold went from 7 to 48 minutes) but not the ranking. Every number on this slide comes from the CLI run.

## Slide 10
THE RECOMMENDATION
Three answers, one for each situation
RECOMMENDED
B · LFP 16S8P, passive
97 min
plug-in → 80 % after a hot ride
Cheapest per kWh (₹18.2 k) and ~3× the life (~1,290 cycles).
Trade-off: 22.7 kg and 13.1 L — misses the mass and volume targets.
IF MASS AND VOLUME ARE HARD LIMITS
A · NMC + Al conduction plate
92 min
plug-in → 80 % after a hot ride
+₹2.7 k and +1.2 kg per pack vs the baseline (13.5 kg).
Most robust: the only design that still passes at 2× unmodelled heat.
RETROFIT FOR PACKS ALREADY BUILT
C · baseline + virtual hotspot sensor
₹0
per pack — BMS settings only
Safe: charge peak 44.5 °C, fixes REQ-03. Slower: 277 vs 244 min, because it waits for the hotspot.
Not AIS-156 compliant: 2 sensors; the rule asks for ≥ 4.
Source: recommend() in packforge/engine.py, printed by the CLI
10
Notes: The tool gives three answers, not one. B is recommended: the cheapest per kWh, about three times the cycle life, 97 minutes — but about 10 kg heavier and bulkier. If mass and volume are hard limits, A: plus ₹2.7 k and 1.2 kg, 92 minutes, and the most robust to extra heat. For the 2-NTC packs already on the road, C is a ₹0 firmware retrofit: it stops hot charging, but it is slower after a hot ride, 277 versus 244 minutes, because it honestly waits for the hotspot. Say clearly: we do not claim AIS-156 compliance for any design; the baseline and C have 2 sensors and Amendment 3, Annex 8K asks for at least 4.

## Slide 11
TOP RISK · ROBUSTNESS
Our pick rests on an unvalidated cell
0.02 K
If cells make 2× the modelled heat, B misses the 45 °C charge limit by 0.02 K — and A becomes the pick. Hold-out data says the model under-predicts the temperature rise ~2×.
Baseline · 339 min
fails REQ-03, REQ-04 (64 °C ride)
A · 132 min
passes — charge peak 45.0 °C
B · 173 min
fails REQ-03 by 0.02 K
C · 392 min
fails REQ-04 (64 °C ride)
At 2× unmodelled heat (BMS not told)
Mitigation: one LFP charge test through the same pipeline — one CSV log decides between B and A.
Source: CLI robustness re-run, cells generate 2× the modelled heat (BMS not told)
11
Notes: This is the slide that earns trust. Our recommended design, B, uses an LFP cell we have not validated — its numbers are generic class values. The hold-out check shows the model under-predicts temperature rise about 2×, so we re-run every design with cells generating twice the modelled heat, without telling the BMS. B then misses the charge limit by 0.02 K and A becomes the pick. That flip is live in the demo with the “Unmodelled heat ×” slider. The fix is cheap: one LFP charge test, run through the same fit pipeline — one CSV.

## Slide 12
PROTOTYPE · LIVE DEMO
The workbench, live, in six steps
1
Baseline after a ride
48 min hold, then REQ-03 fails. Heat map: hot interior vs sensor cells.
2
Option C, the observer
Passes, but slower — the honest trade-off.
3
Compare A and B
The ranking and the three recommendations.
4
Validation
Replay a 45 °C hold-out charge through the calibrated model.
5
Unmodelled heat to 2×
The recommendation flips to A, live.
6
Download the report
One offline HTML file with every figure and finding.
Backup if the app fails: recorded clip of the same path, CLI output and the HTML report.
streamlit run app.py · python -m packforge --report packforge_report.html
12
Notes: Switch to the app now. Follow docs/DEMO_SCRIPT.md: baseline after a ride; Option C; A versus B and the recommendation; the Validation tab replay of a 45 °C hold-out charge; the heat slider to 2×; download the report. If the app does not respond within about 10 seconds, switch to the backup clip and keep talking over it.

## Slide 13
INNOVATION
What a spreadsheet can’t tell you
Cause-explaining conflict checker
Each failure names the subsystems, the cause chain and candidate fixes — not just a red cell.
Sensor blind-spot detection
How far the hottest cell runs above what the BMS acts on, for any sensor count and placement.
Virtual hotspot sensor
A thermal observer in the BMS: a ₹0 retrofit, checked at ±30 % cooling-model error.
Variation Monte Carlo
Cell-to-cell capacity and resistance spread; every sampled pack simulated in one batch.
Evidence-ladder traceability
Requirement → metric → assumption, every number tagged from datasheet up to measured.
PackForge · checks.py · sim.py (observer) · engine.py (Monte Carlo, traceability)
13
Notes: Innovation. Five things a spreadsheet or a single-physics tool will not give you. The conflict checker explains causes across subsystems and proposes fixes. The blind-spot metric makes sensor placement a design variable. The virtual hotspot sensor is a firmware fix you can ship to packs already built. Monte Carlo shows what cell-to-cell spread does to a whole pack. And every number carries its evidence level, so a reviewer knows what is measured and what is assumed.

## Slide 14
BUSINESS VIABILITY
Cheaper packs, fewer prototypes
Chart: Cost per usable kWh (₹)
| B · LFP | Baseline / C | A · NMC + Al
B | 18205 | 0 | 0
Others | 0 | 23149 | 24799
Chart: Estimated cycle life at 40 °C
| B · LFP | A · NMC + Al | Baseline / C
B | 1291 | 0 | 0
Others | 0 | 405 | 370
₹0 retrofit
Option C stops hot charging on packs already built — BMS settings only.
Fewer prototypes
Conflicts surface before hardware; the rig confirms instead of explores.
Reusable
A new cell, option or study is a JSON file, not new code.
Costs and masses are generic class values; cycle life is a rule of thumb — assumptions, not quotes.
Source: PackForge CLI — cost per usable kWh and estimated cycle life to 80 %
14
Notes: Business viability. B is the cheapest per usable kWh and lasts about three times as long in heat, by our estimates — say clearly these use generic class costs and a rule-of-thumb ageing model. C is worth money today: a ₹0 fix for packs already built. And the workbench itself saves prototypes: the blind spot showed up in the model, so a rig test only has to confirm it.

## Slide 15
TECHNICAL FEASIBILITY
Runs on a laptop today
~30 s
The whole study on a laptop: 4 designs, ride then charge, plus the 2× heat re-run.
Open data
Calibrated on a public CC BY 4.0 dataset; anyone can re-run the fit and the hold-out check.
Open stack
Python with numpy, scipy, pydantic, pandas, plotly and Streamlit. CLI, UI and report share one core.
Safe rig
Any bench test stays low-voltage: ≤ 2S protected cells, inline fuse, fireproof bag, never unattended, hard cut‑offs in firmware.
No dataset? The tool still works: every value falls back to a stated assumption with its evidence level.
Timing: one CLI run of studies/escooter_48v on the team laptop (31 s)
15
Notes: Technical feasibility. Nothing here needs a cluster or a licence: the full study, including the robustness re-run, takes about 30 seconds on a laptop. The calibration uses a public dataset under CC BY 4.0. Any hardware test we do next stays low-voltage and supervised: at most 2S, protected cells, an inline fuse, a fireproof bag, never unattended, with hard cut-offs in firmware.

## Slide 16
LIMITATIONS, STATED OPENLY
What we don’t claim
Data and validation
NMC calibrated on a proxy cell in a chamber: single cells, not the cell we would buy, not a pack.
Temperature rise under-predicted ~2×: covered by the 2× re‑run, not fixed.
LFP cell, costs and masses are generic class values. LFP is not validated.
Ageing is a rule of thumb, not validated.
Below 10 % SOC the voltage error grows to ~0.1–0.9 V near cut-off.
Model and scope
Lumped thermal model with an effective h; no CFD, no enclosure air node.
One node per cell: on the proxy cell the core runs up to 4.6 K above the surface.
The observer shares the plant’s model structure; real error will exceed the ±30 % we test.
Synthetic drive profile, not a homologation cycle. One 48 V pack only.
No design is claimed AIS-156 compliant (Amd. 3, Annex 8K asks for ≥ 4 sensors).
Source: ROADMAP.md — known limitations
16
Notes: Say these before the judges ask. The NMC evidence is measured on a proxy cell, not our cell and not a pack. The temperature rise is under-predicted about 2× — which is exactly why the robustness run exists. LFP is not validated. The thermal model is lumped, one node per cell. And we make no AIS-156 compliance claim for any design.

## Slide 17
CLOSE
Build B, keep A ready, ship C today
Recommendation
B
B (LFP) for new packs: 97 min, cheapest per kWh, ~3× the life — if 22.7 kg is acceptable.
A
A (NMC + Al plate) if mass and volume are hard limits, or if the LFP test shows more heat.
C
C (firmware, ₹0) for 2-NTC packs already built: safe, slower after a hot ride.
Next steps
1
One LFP charge test through the same fit pipeline — one CSV decides B or A.
2
A pack-level log to check the blind spot and the core-to-surface gap on real hardware.
3
Our ask: LFP cells and supervised rig time to run step 1 safely (≤ 2S, fused, never unattended).
PackForge: a small, working, validated workbench — with its risks stated.
Falak Anwar · office.falakanwar@gmail.com · Zaid Alam · zaidlc319@gmail.com
17
Notes: Close on the decision, not the tool. Build B for new packs; keep A ready because it is the robust choice if the LFP cell runs hotter than modelled; and ship C to the packs already on the road, at no hardware cost. The next step is cheap and decisive: one LFP charge test through the same pipeline, then a pack-level log. Our ask is small and concrete: LFP cells and supervised rig time to run that test safely.

## Slide 18
SOURCES AND ATTRIBUTION
Where every number comes from
Measured data (proxy cell)
Jiaqi Yao, Droese, Kowal, “Lithium-Ion Battery Internal Temperature Dataset”, Technische Universität Berlin, EET, 2026. DOI 10.14279/depositonce-25110, licensed CC BY 4.0. LG INR21700 M50LT cells. Our changes: current sign flipped, columns renamed, values rounded, charges cut and resampled to 1 s.
Generic cell values
NMC 21700 5 Ah and LFP cells are “class” values, not a named datasheet. Costs and masses are assumptions, each with an ID in the design files.
Not evidence
SYNTHETIC_* logs are generated by our own model — a method check for the fitter, never validation.
Brief and regulation
TELIPORT Season 4 (Tata Elxsi), Case Study 2: Reusable Digital Platform for Designing Battery Energy System. AIS-156 Amd. 3, Annex 8K (cited, no compliance claimed).
data/validation/SOURCES.md · data/validation/calibration_nmc21700_5ah.json
18
Notes: Leave this slide up during questions if there is time. The dataset attribution is required by its CC BY 4.0 licence.