## Slide 1
TELIPORT Season 4 · Tata Elxsi · Case Study 2: Reusable Digital Platform for Designing Battery Energy System
PackForge · Falak Anwar · Zaid Alam
PackForge shows that a 48 V scooter pack charges hidden cells at 47.6 °C after a hot ride, and ranks three fixes before any hardware is built
The problem Problem understanding · Desirability
48 V e-scooter pack (13S10P NMC, 2,263 Wh) at 40 °C, plugged in straight after the ride
Edge NTCs read 3.2 K low; after a 48 min hold the BMS charges interior cells at 47.6 °C (limit 45 °C)
For students learning why designs fail and pack engineers choosing what to prototype
The platform Feasibility · Innovation
One design file feeds an electro-thermal sim, a sensor-only BMS and a conflict checker (11 requirements, 14 interface rules)
New: cause chains with fixes, blind-spot metric, virtual hotspot sensor, evidence levels
31 s per study on a laptop; a new option is one JSON file
The evidence Engineering quality · Prototype
Cell fitted on public TU Berlin data (proxy cell LG M50LT) at 25 and 35 °C
60 hold-out logs at 45 °C: voltage RMSE 17–18 mV (median)
Heating underestimated ~2×, so every design is re-run at 2× heat
23 automated tests incl. heat balance and a hand‑calc bound
Chart: Charge time, plug-in → 80 % after a 40 °C ride (min)
| Baseline · 244 min | A: NMC + Al plate · 92 min | B: LFP 16S8P · 97 min | C: + BMS observer · 277 min
Thermal hold (no current) | 48.2 | 0 | 0 | 89.5
Charging | 195.5 | 92.1 | 97.4 | 187.1
120 min limit
Recommendation Business viability
B · LFP for new packs: 97 min, ₹18.2 k per usable kWh (lowest), ~3× cycle life (estimate); over mass and volume targets
A · NMC + Al plate if mass is capped: 92 min, +₹2.7 k per pack; the only design that passes at 2× heat
C · BMS observer for packs already built: ₹0, safe at 44.5 °C, 277 min
Top risk: the LFP cell is not validated; at 2× heat B misses the limit by 0.02 K and A becomes the pick
Next step: a supervised LFP charge test (≤ 2S, fused) decides B or A
Data: Yao, Droese & Kowal (2026), TU Berlin, DOI 10.14279/depositonce-25110, CC BY 4.0. Costs and masses are generic class values. No design is claimed AIS‑156 compliant. github.com/gitFa07/battery-energy-system · office.falakanwar@gmail.com · zaidlc319@gmail.com
Notes: One-slider for the initial submission. Every number comes from the CLI run of studies/escooter_48v and the calibration record, the same sources as docs/PackForge_pitch.pptx.